Task 1

Initial Benchmark:
time ./gpurender
real	0m2.509s
user	0m2.422s
sys	0m0.020s

time ./gpurender -g
real	0m7.073s
user	0m6.998s
sys	0m0.008s

a)
For this I used 8k resolution, to get the needed amount of runtime.
time ./gpurender -v=4320 -w=7680 -d=3
real	0m21.405s
user	0m20.860s
sys	0m0.120s

Timing workQueue:
time ./gpurender -v=4320 -w=7680 -d=3
Runs:
1: 11.2017s
2: 11.1944s
3: 11.2167s

b)

Here I simply added #pragma omp parallel for to the loop iterating over the workQueue.
time ./gpurender -v=4320 -w=7680 -d=3

c)

Simpy applying the #pragma omp parallel for, the program becomes much slower, and the output image is completely ruined.

This fix to this race condition was to remove the reference to transformedMesh in rasteriseTriangles. This change results in a correct output image (same md5sum), and a much faster execution time. This is a race condition because you send the reference into the other methods, which means several threads can have the same reference, causing the image to get distorted. I was also able to fix the race condition by adding a mutex in rasteriseTriangles around the face.getDepth(u,v,w); call, however this made the program very slow, though it did fix the race condition.

d)
time ./gpurender -v=4320 -w= 7680 -d=3

Static (standard):
real	0m12.474s
user	0m25.963s
sys	0m0.136s
Time spent iterating workQueue: 2.52676

Dynamic:
real	0m12.056s
user	0m26.689s
sys	0m0.136s
Time spent iterating workQueue: 2.28222

Guided:
real	0m12.199s
user	0m26.156s
sys	0m0.109s
Time spent iterating workQueue: 2.3951

Changing the scheduling strategy did not seem to impact performance much, dynamic might be slightly faster.

e)

Without OpenMP: ~11.2s, comparing workQueue times.

Static: 4.4x faster.
Dynamic: 4.9x faster.
Guided: 4.7x faster.

f)

Since the items computed have a similar amount of computation associated with each, I would not expect a specific schedule to be faster than another. You can expect some strategies to be faster than others if part of the work further along in the queue is slower than previous entries, however in this case this is not the case. Therefore I would not really expect any strategy to be faster than others.

Task 2

a)

b)

As we can see this lab pc has a GTX 1080 Ti.

c)

Task 3

a)

I was not really sure what you asked here, since each loop is nested. Obviously the other loop takes the longest, and the inner loop take some portion of that time, in my case the second loop had 5 elements, and thereby took about 1/5 the time of the outer loop with each iteration, as measured with std::chrono.

b)

For my strategy, I decided to convert the outer loops to device, since they are the ones which take up the most time. I will leave the rest of the loops intact. The first two loops can be separated into blocks and threads, meaning we can easily eliminate these loops.

Task 4

a)

b)

And I did the equivalent for depthBuffer.

c)

d)

Task 5

a)

Since it was fairly easy to get blockId and threadId, I decided to only convert the outer two loops. You could also convert the third loop by doing some index calculation (like the one commented out in my code), however I could not quite get that to work, so I just went with the two outer loops. To get this to run I simply had to add __device__ to runVertexShader and rasteriseTriangle, and delete other usages of these functions outside of the device context.

b)

Task 6

a)

One potential race condition I found was that vertex.x, and .y was set twice in runVertexShader, using itself as an argument, this means another thread could potentially override the vertex which would alter the image. I changed this by putting the first operation inside the other, eliminating the need to use vertex as an argument for its own new assignment.

This fixes some minute errors in the image, however there are still some other errors, probably because of other race conditions. Another suspect for a race condition I found is in rasteriseTriangle, where depthBuffer is accessed and written to several times, which probably causes a race condition, I was however unable to fix this one, or my changes seemed to have no effect on the output image.

b)

OpenMP measurements:
time ./gpurender -v=4320 -w=7680 -d=3
Dynamic:
real	0m12.056s
user	0m26.689s
sys	0m0.136s
Time spent iterating workQueue: 2.28222

GPU measurements:
time ./gpurender -v=4320 -w=7680 -d=3 -g

real	0m10.534s
user	0m9.593s
sys	0m0.537s
Time spent rendering on GPU (device_renderMeshes call): 1.15223

The rendering time has been improved by almost 98%!

Including allocating and copying buffers, I got a total time of 1.28356s. I did this by using std::chrono and adding to a total_time variable for each operation.

This brings the speedup to 77% instead of 98%.